## Slide 1: 7. MOMENT DISTRIBUTION METHOD

## Slide 2: 7.1 MOMENT DISTRIBUTION METHOD - AN OVERVIEW
7.1 MOMENT DISTRIBUTION METHOD - AN OVERVIEW
7.2 INTRODUCTION
7.3 STATEMENT OF BASIC PRINCIPLES
7.4 SOME BASIC DEFINITIONS
7.5 SOLUTION OF PROBLEMS
7.6 MOMENT DISTRIBUTION METHOD FOR STRUCTURES HAVING NONPRISMATIC MEMBERS

## Slide 3
7.2 MOMENT DISTRIBUTION METHOD -
INTRODUCTION AND BASIC PRINCIPLES
7.1 Introduction
(Method developed by Prof. Hardy Cross in 1932)
The method solves for the joint moments in continuous beams and
rigid frames by successive approximation.
7.2 Statement of Basic Principles
Consider the continuous beam ABCD, subjected to the given loads,
as shown in Figure below. Assume that only rotation of joints occur
at B, C and D, and that no support displacements occur at B, C and
D. Due to the applied loads in spans AB, BC and CD, rotations occur at B, C and D.
15 kN/m
10 kN/m
150 kN
8 m
6 m
8 m
A
B
C
D
I
I
I
3 m

## Slide 4
In order to solve the problem in a successively approximating manner,
it can be visualized to be made up of a continued two-stage problems
viz., that of locking and releasing the joints in a continuous sequence.
7.2.1 Step I
The joints B, C and D are locked in position before any load is applied on the beam ABCD; then given loads are applied on the beam. Since the joints of beam ABCD are locked in position, beams AB, BC and CD acts as individual and separate fixed beams, subjected to the applied loads; these loads develop fixed end moments.
8 m
-80 kN.m
-80 kN.m
15 kN/m
A
B
6 m
-112.5kN.m
112.5 kN.m
B
C
8 m
-53.33 kN.m
10 kN/m
C
D
150 kN
53.33 kN.m
3 m

## Slide 5
In beam AB
Fixed end moment at A = -wl2/12 = - (15)(8)(8)/12 = - 80 kN.m
Fixed end moment at B = +wl2/12 = +(15)(8)(8)/12 = + 80 kN.m
In beam BC
Fixed end moment at B = - (Pab2)/l2 = - (150)(3)(3)2/62
= -112.5 kN.m
Fixed end moment at C = + (Pab2)/l2 = + (150)(3)(3)2/62
= + 112.5 kN.m
In beam AB
Fixed end moment at C = -wl2/12 = - (10)(8)(8)/12 = - 53.33 kN.m
Fixed end moment at D = +wl2/12 = +(10)(8)(8)/12 = + 53.33kN.m

## Slide 6
7.2.2 Step II
Since the joints B, C and D were fixed artificially (to compute the the fixed-end moments), now the joints B, C and D are released and allowed to rotate. Due to the joint release, the joints rotate maintaining the continuous nature of the beam. Due to the joint release, the fixed end moments on either side of joints B, C and D act in the opposite direction now, and cause a net unbalanced moment to occur at the joint.
15 kN/m
10 kN/m
8 m
6 m
8 m
A
B
C
D
I
I
I
3 m
150 kN
Released moments -80.0
-112.5
+53.33
-53.33
+112.5
Net unbalanced moment
+32.5
-59.17
-53.33

## Slide 7
7.2.3 Step III
These unbalanced moments act at the joints and modify the joint moments at B, C and D, according to their relative stiffnesses at the respective joints. The joint moments are distributed to either side of the joint B, C or D, according to their relative stiffnesses. These distributed moments also modify the moments at the opposite side of the beam span, viz., at joint A in span AB, at joints B and C in span BC and at joints C and D in span CD. This modification is dependent on the carry-over factor (which is equal to 0.5 in this case); when this carry over is made, the joints on opposite side are assumed to be fixed.
7.2.4 Step IV
The carry-over moment becomes the unbalanced moment at the joints to which they are carried over. Steps 3 and 4 are repeated till the carry-over or distributed moment becomes small.
7.2.5 Step V
Sum up all the moments at each of the joint to obtain the joint moments.

## Slide 8
7.3 SOME BASIC DEFINITIONS
In order to understand the five steps mentioned in section 7.3, some words need to be defined and relevant derivations made.
7.3.1 Stiffness and Carry-over Factors
Stiffness = Resistance offered by member to a unit displacement or rotation at a point, for given support constraint conditions
A
MA
MB
A
B
A
RA
RB
L
E, I – Member properties
A clockwise moment MA is applied at A to produce a +ve bending in beam AB. Find A and MB.

## Slide 9
Using method of consistent deformations
L
A
A
MA
B
L
fAA
A
B
1
Applying the principle of consistent deformation,
Stiffness factor = k = 4EI/L

## Slide 10
Considering moment MB,
MB + MA + RAL = 0
MB = MA/2= (1/2)MA
Carry - over Factor = 1/2
7.3.2 Distribution Factor
Distribution factor is the ratio according to which an externally applied unbalanced moment M at a joint is apportioned to the various members mating at the joint
+ ve moment M
A
C
B
D
A
D
B
C
MBA
MBC
MBD
At joint B
M - MBA-MBC-MBD = 0
I1
L1
I3
L3
I2
L2
M

## Slide 11
i.e., M = MBA + MBC + MBD

## Slide 12
7.3.3 Modified Stiffness Factor
The stiffness factor changes when the far end of the beam is simply-supported.
A
MA
A
B
RA
RB
L
As per earlier equations for deformation, given in Mechanics of Solids text-books.

## Slide 13
7.4 SOLUTION OF PROBLEMS -
7.4.1 Solve the previously given problem by the moment distribution method
7.4.1.1: Fixed end moments
7.4.1.2 Stiffness Factors (Unmodified Stiffness)

## Slide 14
7.4.1.3 Distribution Factors

## Slide 15
7.4.1.4 Moment Distribution Table

## Slide 16
7.4.1.5 Computation of Shear Forces
8 m
3 m
3 m
8 m
I
I
I
15 kN/m
10 kN/m
150 kN
A
B
C
D

## Slide 17
7.4.1.5 Shear Force and Bending Moment Diagrams
56.23
3.74 m
75.563
63.77
52.077
74.437
27.923
2.792 m
-69.806
98.297
35.08
126.704
-96.613
31.693
Mmax=+38.985 kN.m
Max=+ 35.59 kN.m
3.74 m
84.92
-99.985
48.307
2.792 m
S. F. D.
B. M. D

## Slide 18
Simply-supported bending moments at center of span
Mcenter in AB = (15)(8)2/8 = +120 kN.m
Mcenter in BC = (150)(6)/4 = +225 kN.m
Mcenter in AB = (10)(8)2/8 = +80 kN.m

## Slide 19
7.5 MOMENT DISTRIBUTION METHOD FOR NONPRISMATIC MEMBER (CHAPTER 12)
The section will discuss moment distribution method to analyze beams and frames composed of nonprismatic members. First the procedure to obtain the necessary carry-over factors, stiffness factors and fixed-end moments will be outlined. Then the use of values given in design tables will be illustrated. Finally the analysis of statically indeterminate structures using the moment distribution method will be outlined

## Slide 20
7.5.1 Stiffness and Carry-over Factors
Use moment-area method to find the stiffness and carry-over factors of the non-prismatic beam.

A
B
PA
MB
MA
A
CAB= Carry-over factor of moment MA from A to B

## Slide 21
A
B
MA=CBAMB
=CBAKB
MB(KB)
MB=CABMA
=CABKA
MA(KA)
A (= 1.0)
MA
B (= 1.0)
A
B
(a)
(b)
Use of Betti-Maxwell’s reciprocal theorem requires that the work done by loads in case (a) acting through displacements in case (b) is equal to work done by loads in case (b) acting through displacements in case (a)
MB

## Slide 22
7.5.2 Tabulated Design Tables
Graphs and tables have been made available to determine fixed-end moments, stiffness factors and carry-over factors for common structural shapes used in design. One such source is the Handbook of Frame constants published by the Portland Cement Association, Chicago, Illinois, U. S. A. A portion of these tables, is listed here as Table 1 and 2
Nomenclature of the Tables
aA ab = ratio of length of haunch (at end A and B to the length of span
b = ratio of the distance (from the concentrated load to end A) to the length of span
hA, hB= depth of member at ends A and B, respectively
hC = depth of member at minimum section

## Slide 23
Ic = moment of inertia of section at minimum section = (1/12)B(hc)3, with B as width of beam
kAB, kBC = stiffness factor for rotation at end A and B, respectively
L = Length of member
MAB, MBA = Fixed-end moments at end A and B, respectively; specified in tables for uniform load w or concentrated force P
Also